# Connectors and Pinout
## Linear motor side
### Stator side with Speedtec M23 and M17
PIN	FUNCTION	CONNECTOR VIEW FRONT	PIN	FUNCTION
12	SIN+/SLO+	m23_m17_connector.jpg	1	U
11	SIN-/SLO-	2	V
10	COS+/MA-	Earth	PE
9	COS-/MA+	4	-
8	PTC-/A-	5	-
7	PTC+/A+	6	W
6	+5VDC
5	GND
4	-
3	-/B-
2	-/B+
1

Connectors: Intercontec Speedtec AEDC047NN0000051A000 (M17) + BEDC106NN00000201000 (M23)
## Rotary motor side
Encoder type: Resolver 2p 7V 10KHz
Function	Pin
Ref+	10
Ref-	7
Cos+	2
Cos-	1
Sin+	11
Sin-	12
PTC+ Sensor	8
PTC- Sensor	9

## M23 type connectors
m23_1.jpg	m23_2.jpg	m23_3.jpg	m23_4.jpg
Fixed side Feeedback E - external view	Flying side Feedback P - external view	Fixed side Motor phases - external view	Flying side Motor phases - external view
	ASTA 014 - 09010005		BSTA 085 - 09020004

Function	Pin
U	1
V	2
W	6
PE	Earth
-	4
-	5