# Mechanical Dimensions

encoder_view.jpg
Encoder Model	La	Lt
Revenc_736	736	856
Revenc_660	660	780

La is the Active Encoder Area where the sensor detect the position of the reference magnet.
Lt is the total length of encoder excluding the connector.
## LED indicators
Condition	LED Green	LED Orange	LED Red
Normal operation	Dimming	-	-
Normal operation communicating with Hiperface RS485 interface	Dimming	Blinking	-
Encoder fault (SIN/COS under-range)	Dimming	-	ON
Boot phase (LED cycling) - duration from Reset 5 seconds	ON → OFF	ON → OFF	ON → OFF
Calibration active	Dimming	Blinking	-

## 3D step models
Revend_736: :reverso_encoder:revenc_encoder_-_profile_736mm.zip