# Power cable
The linear stage is equipped with 1 meter cable with M23 standard speedtec connector at the cable end.

power_cable.jpg
## Pinout - Power connector BKUA145NN00420200400 (Serie 923 - 9 poles)

PIN	Signal
A	U phase
B	V phase
C	W phase
D/PE	Protection Earth
F	Thermal switch+
G	Thermal switch-
L	not connected
H	not connected
CASE	Shield