# ULCV 132

## Mechanical Drawing

## Load rating

## Technical data
Parameter	Symbol	Value	Unit
Max usable stroke		6500	mm
Total lenght	Ltot	C+Lc+190	mm
Carriage length	Lc	230	mm
Carriage usable length	Lu	220	mm
Extra-stroke (safety)	Ec	60	mm
Max speed		180	m/min
Max acceleration		100	m/sec2
Position repeatability		< 0.05	mm
Aluminium profile section		132 x 71 x 5	mm
Inertia momentum of aluminium profile	Ix	1413267	mm4
Inertia momentum of aluminium profile	Iy	2429437	mm4
Type of mechanic		linear guide with compact block
Belt type		Poliuretan HTD-5M-75
Pulley teeth number		36
Diameter		57,3	mm
Linear movement per rotation		180	mm
Operating temperature		-20 / +60	degrees